## Slide 1: Electric Bicycle Project
Alec Korver | Chris Slice | Bryan Hanenburg
Professor De Boer - Project Mentor
Professor Schuurman - Customer
Notes: Good afternoon everyone, Alec Korver, Chris Slice, and I, Bryan Hanenburg are the electric bike design team.

## Slide 2: Introduction
Problem
  Inefficient
  Pollutes Environment
  Expensive
http://cdn.zmescience.com/wp-content/uploads/2013/09/traffic.jpg
Notes: According to the United States Department of Transportation the average driver travels 29 miles per day. Nearly 90% of these daily trips are taken in personal motor vehicles. For most people, comfort, time, and convenience are the most important factors in determining how they travel each day. These preferences often equate to each person driving a heavy and inefficient vehicle to work or school. By doing so we waste 90 times more energy that if we walk or bike. This not only pollutes the air around us, but can be a significant expense as well. Being mindful of this wastefulness is an excellent start, but most people also need faster travel alternatives than running or biking.

## Slide 3: Introduction
http://www.energybc.ca/images/profiles/wind/windfarm.jpg
Solution
  Eco-Friendly
  Enjoyable
  Affordable
  Healthy
Notes: Our team’s goal was to address these shortcomings by offering an realistic, yet attractive solution. We did not want to reinvent the wheel, but to use existing technology to create a more eco-friendly, enjoyable, affordable, and healthy alternative.

## Slide 4: Introduction
Our Electric Bicycle
  Eco-Friendly
  Enjoyable
  Affordable
  Healthy
Notes: Our solution is FLUX.
FLUX is an electric bicycle that we designed, simulated, and built for use in Northwest Iowa. Flux is an improvement to the everyday drive and it was hand built using primarily off the shelf components. Because of this we are able to make sure that the final product is, durable, quick to assemble, low maintenance, and easy to repair. But to ensure that the components we chose were ideal for our application, we needed to follow a systematic approach so that we would have a favorable outcome.

## Slide 5: Introduction
Our Approach
  Computer Simulation
  Bike Design
  Design Verification
Notes: To achieve this, we first created a computer simulation that took into account all the individual pieces of the bicycle to see what worked best. We then created the bicycle from the parts we chose, and conducted various tests to ensure that the simulation was accurate, and that the bike performed as expected.

## Slide 6: Early Design Simulation
What is a simulation?
Virtual (Computer based) representation of our bicycle design.
What does it do?
Helps predict maximum range, top speed, and battery consumption.
Notes: So what is a simulation? A simulation is a virtual or computer based program which can be used to mathematically model real world objects or phenomenon. In the context of our project our simulation helps us compare many different bicycle designs and helps us to determine how far the bike will go, how fast you can travel, and how much battery power will be used. [next slide]

## Slide 7: Early Design Simulation
Notes: Our first program was Aptly named Early Simulation. This simulation focused on providing an in depth understanding of the operational physics of various electric bicycle configurations by allowing us to tweak wheel size, gearing ratios, motor types, and battery voltages. Early Simulation allowed us to model and test multiple electric bicycle designs. Early simulation allowed us to change the variables in order to evaluate the bicycle as a whole. Each design was run on a “riding profile” and the differences in efficiency, top speed, time it took to complete, were compared. [next slide]

## Slide 8: Early Design Simulation
Notes: For our early design and simulation phase we used a riding path from orange city to sioux center. We were able to easily determine the performance differences between our various bicycle designs by comparing all of our designs against this same riding profile.

## Slide 9
Chart: Torque (Nm) & Power (W) Vs Speed (RPM)
| 228.3666666666666 | 214.2699588477366 | 200.1732510288059 | 186.076543209876 | 171.9798353909465 | 157.8831275720165 | 143.7864197530864 | 129.6897119341562 | 115.5930041152263 | 101.4962962962963 | 87.39958847736625 | 73.30288065843607 | 59.20617283950616 | 45.10946502057613 | 31.01275720164609 | 16.91604938271605 | 2.819341563786008 | -12.68703703703704
1st Gear | 0 | 6.0586 | 12.1172 | 18.1758 | 24.2344 | 30.293 | 36.3516 | 42.4102 | 48.4688 | 54.5274 | 60.5859 | 66.6445 | 72.7031 | 78.7617 | 84.8203 | 90.8789 | 96.9375 | 102.9961
2nd Gear | 0 | 4.9579 | 9.9158 | 14.8737 | 19.8315 | 24.7894 | 29.7473 | 34.7052 | 39.6631 | 44.621 | 49.5789 | 54.5368 | 59.4946 | 64.4525 | 69.4104 | 74.3683 | 79.3262 | 84.2841
3rd Gear | 0 | 4.2686 | 8.5371 | 12.8057 | 17.0742 | 21.3428 | 25.6113 | 29.8799 | 34.1484 | 38.417 | 42.6856 | 46.9541 | 51.2227 | 55.4912 | 59.7598 | 64.0283 | 68.2969 | 72.5654
4th Gear | 0 | 3.7519 | 7.5038 | 11.2557 | 15.0077 | 18.7596 | 22.5115 | 26.2634 | 30.0153 | 33.7672 | 37.5191 | 41.2711 | 45.023 | 48.7749 | 52.5268 | 56.2787 | 60.0306 | 63.7825
5th Gear | 0 | 3.1929 | 6.3858 | 9.5786 | 12.7715 | 15.9644 | 19.1573 | 22.3502 | 25.543 | 28.7359 | 31.9288 | 35.1217 | 38.3146 | 41.5074 | 44.7003 | 47.8932 | 51.0861 | 54.2789
6th Gear | 0 | 2.6107 | 5.2214 | 7.8321 | 10.4428 | 13.0535 | 15.6642 | 18.2749 | 20.8856 | 23.4963 | 26.1069 | 28.7176 | 31.3283 | 33.939 | 36.5497 | 39.1604 | 41.7711 | 44.3818
7th Gear | 0 | 2.2501 | 4.5002 | 6.7503 | 9.0004 | 11.2505 | 13.5005 | 15.7506 | 18.0007 | 20.2508 | 22.5009 | 24.751 | 27.0011 | 29.2512 | 31.5013 | 33.7514 | 36.0015 | 38.2515
8th Gear | 0 | 1.977 | 3.954 | 5.931 | 7.9081 | 9.8851 | 11.8621 | 13.8391 | 15.8161 | 17.7931 | 19.7702 | 21.7472 | 23.7242 | 25.7012 | 27.6782 | 29.6552 | 31.6322 | 33.6093
Power 1st Gear | 0 | 135.9488 | 254.0095 | 354.1823 | 436.4671 | 500.8639 | 547.3727 | 575.9935 | 586.7263 | 579.5711 | 554.5279 | 511.5967 | 450.7775 | 372.0703 | 275.4751 | 160.992 | 28.6208 | -136.8432
Power 2nd Gear | 0 | 135.9488 | 254.0095 | 354.1823 | 436.4671 | 500.8639 | 547.3727 | 575.9935 | 586.7263 | 579.5711 | 554.5279 | 511.5967 | 450.7775 | 372.0703 | 275.4751 | 160.992 | 28.6208 | -136.8432
Power 3rd Gear | 0 | 135.9488 | 254.0095 | 354.1823 | 436.4671 | 500.8639 | 547.3727 | 575.9935 | 586.7263 | 579.5711 | 554.5279 | 511.5967 | 450.7775 | 372.0703 | 275.4751 | 160.992 | 28.6208 | -136.8432
Power 4th Gear | 0 | 135.9488 | 254.0095 | 354.1823 | 436.4671 | 500.8639 | 547.3727 | 575.9935 | 586.7263 | 579.5711 | 554.5279 | 511.5967 | 450.7775 | 372.0703 | 275.4751 | 160.992 | 28.6208 | -136.8432
Notes: Additionally, Early Simulation allowed us to look at torque speed curves of different bicycle gearing ratios. From this graph we can also see where each gearing step falls in its associated power band. With higher RPMS being associated with higher efficiency levels and lower RPMs being associated with more torque. After the accuracy of Early Simulation was verified, we then proceeded to develop our web based simulation.[next slide]

## Slide 10: Web Based Simulation
What’s the purpose of our Web based Simulation?
  Designing customizable bikes. Not everyone needs:
    20Ah Battery
    1300W motor
  Provide trip data
    Trip distance and time
    Energy used, % battery
    remaining
Notes: Whats the purpose of our web based simulation?
It is a simplified version of our early simulation. It gives everyone the ability to simulate their unique bicycle on their unique commute. This is valuable for designers as well as users. Not everyone needs the 20ah battery or 1300 w motor that we used in our bike. Since this simulation is easily repeatable with variable parts, it allows us to determine the ideal configurations for different customers. We can determine what parts make the best bike for my parents, who might use the bike primarily in town, or for me, who might use it to make 20 mile trips to hull and back for Sunday dinner. We can guarantee that the bike will do what the customer need it too, and that customers aren’t paying more for a bike which provide a range or speed that they don’t use.
-This simulation served a double purpose by providing information to users. We believed it was necessary to provide this data to riders, and this simulationwas the best way to accomplish this goal within our allocated resources.

## Slide 11: Web Based Simulation
Try it yourself at homepages.dordt.edu/chrsslc
Notes: What about the program itself?
Start the video now
A User navigates to our webpage via any internet accessible device, and inputs the characterisitcs of their real or theoretical bicycle. They then choose their route from anywhere in the world . The user can, on a turn by turn basis, define their path. The program corrects the estimated route to fit the road’s twists and turns. This simulation is technically easy to use. It predicts and records the time and distance traveled and % battery reamining.

## Slide 12: Web Based Simulation
    Minimizes
    Cost
    Maximizes Responsibility
    Proves
    Feasibility
  How does it solve problems?

## Slide 13: Validation & Testing
Tested potential commutes
Compared data to simulation
Ensured difference < 10%
  Ensuring Accuracy
Notes: Since an inaccurate simulation is not useful to our potential users, we needed to ensure that it was accurate in a variety of conditions. We did this by attaching monitoring electronics between the motor and the battery, and then rode along potential commutes between Sioux Center, Orange City, and Hull. The results after each trip were recorded and then compared to the simulation. We hoped to keep the difference in energy consumption between the simulation and the tests under 10% due to the affect of wind and other road conditions. We consistently stayed within 5-7% of the predicted value, so we can safely conclude that the simulation is accurate.

## Slide 14: Battery Box
Needed to:
  Protect the battery and electrical connections
  Allow charging of battery
  Have a keyed switch
  Be waterproof
Notes: The main piece of the bicycle unaffected by the simulation results, was the battery box. This is important for several reasons, as these increase the reliability, safety, and convenience of using the bicycle. The final design was a custom built aluminum box that fits into the center of the frame. This was chosen primarily due to a lack of commercially available options that fulfilled the requirements above, which were all easily obtainable with a custom solution.

## Slide 15
Credit goes to Ben Kuiper for filming and editing this video.
Notes: Bring out bike after promo video

## Slide 16: Questions?

## Slide 19: Groschopp Testing & Validation
Notes: We used our testing as a means to increase our simulation accuracy

## Slide 20: Final Design
750W Mid Drive Electric Motor
20.8 AH 52V Battery
Aluminum Battery Box
6061 Aluminum Frame
8-Speed Internally Geared Hub
26” Hybrid Commuter Wheels

## Slide 21
Chart: Groschopp Test Data vs Simulation
| 0.0 | 0.035477236410562 | 10.58102926703545 | 22.8003385593994 | 34.686342605231 | 45.7475573969317 | 56.9217570179654 | 68.581791405131 | 78.63744121576798 | 92.45548584319377 | 102.5450311026308 | 113.775723138331 | 126.54300885296
Current Test | 1.19 | 1.157 | 4.599 | 7.54 | 10.583 | 13.623 | 16.33 | 19.108 | 21.834 | 24.485 | 24.496 | 24.667 | 24.614
RPM Test | 139.2 | 141 | 134 | 128 | 124 | 120 | 114 | 114 | 104 | 107 | 90 | 78 | 64
Current Simulation | 1.594 | 1.603 | 4.2816 | 7.3853 | 10.4043 | 13.2139 | 16.0521 | 19.0138 | 21.5679 | 24.2537 | 24.2537 | 24.2537 | 24.2537
RPM Simulation | 141 | 140.9874 | 137.2437 | 132.9059 | 128.6863 | 124.7596 | 120.7928 | 116.6535 | 113.0837 | 110.6364 | 99.029 | 86.1089 | 71.421
Power Input Test | 63.2 | 61 | 242 | 394.6 | 549.3 | 701 | 833.2 | 966.3 | 1094 | 1216.1 | 1214.7 | 1221.2 | 1217.1
Power Output Test | 0 | 0.52384 | 148.4786 | 305.6205 | 450.4134 | 574.8841 | 679.5389 | 818.7378 | 856.4339 | 1035.971 | 966.4698 | 929.3416 | 848.1043
Power Input Simulation | 85.5854 | 86.0671 | 228.1989 | 390.2559 | 545.1799 | 686.9503 | 827.8165 | 972.2866 | 1094.8106 | 1206.6593 | 1205.0534 | 1203.2658 | 1201.2336
Power Output Simulation | 0 | 0.52381 | 152.0767 | 317.342 | 467.4478 | 597.7011 | 720.0479 | 837.8158 | 931.2612 | 1071.2052 | 1063.4554 | 1025.9821 | 946.4689
Notes: Knowing that we had an accurate model was important. From this we decided to develop a web based simulation.